## Slide 1: Natural Gas Emissions from the Heavy and Medium Duty Trucking Sectors Quantifying methane emissions at fueling and maintenance facilities
Nigel Clark, Principal Investigator
Nigel.Clark@mail.wvu.edu, 304 293-4813
W. Scott Wayne, David McKain, Hailin Li, Daniel Carder
Co-Principal Investigators
Center for Alternative Fuels, Engines and Emissions
West Virginia University
Morgantown, WV USA
August 21, 2012

## Slide 2: Center for Alternative Fuels, Engines and Emissions: CAFEE
West Virginia University Land Grant Institution with Strong Applied Research Record
  Benjamin M. Statler College of Engineering and Mineral Resources
    Department of Mechanical and Aerospace Engineering
      Center for Alternative Fuels, Engines and Emissions (CAFEE)

## Slide 3: CAFEE: Research Experience
Research Areas
  Tailpipe Emissions
  Exhaust Plume Characterization
  Dual Fuel Engine Research
  Engine/Vehicle Driving Cycle Development
  Emissions Modeling
  Vehicle Activity Studies
  Engine Design
  Fuels Evaluation
  Life-Cycle Cost Modeling
Over $70 million in funded research over the past two decades

## Slide 4: Fugitive Methane Emissions
Fugitive Sources: Fueling and Maintenance
  Unintentional
    Leaks
      Continuous
      Intermittent
      Failure
      Poor Assembly
    Refueling
    Disaster
  Intentional
    LNG boil-off
    Pressure relief
    Discharge

## Slide 5: Relevant Emissions Levels
Natural gas methane emissions are considered
At higher level of loss economic impact becomes important
Carbon dioxide emissions from natural gas trucks are 0-25% lower than from conventional diesel trucks
We have selected a 5% carbon dioxide equivalent impact as a criterion
We have assumed, simplistically, that methane is equivalent to 20x carbon dioxide by mass
5

## Slide 6: Fueling Station Loss Impact Analysis
Based on methane being equivalent to 20x carbon dioxide by mass, a 0.4% discharge methane has the same GHG impact as a 5% increase in carbon dioxide emissions
Consider a fueling facility that dispenses 1000 kilograms per day of natural gas
  0.4% loss represents (assuming 100% methane)
    4 kilograms (5,600 liters, 198 cubic feet) per day
    2.8 grams (3.8 liters, 0.137 cubic feet) per minute
    0.047 grams per second (0.063 liters, 0.0022 cubic feet) per second
We therefore need to be able to quantify this level of loss with reasonable accuracy
6

## Slide 7: Methods for Quantification
Component Based
  Identify all leaks/discharges, whether continuous or intermittent
  Quantify the leaks/discharges through enclosure/hi-volume sampling
  Determine frequencies of intermittent discharges
  Sum the quantities to determine daily loss rate
Station Based
  Tent/Enclose entire facility and determine loss by measuring concentration and through-flow
  Suitable for small facilities
Atmospheric Based
  Use atmospheric sampling techniques to estimate loss
Station inventory (mass balance)
  Measure difference between fuel supplied to station and fuel delivered to vehicles
  Relies on ability to measure natural gas accurately
  NG fueling industry using micro motion flow meters: +/- 0.5% of fuel delivered
7

## Slide 8: Methane Quantification: High Volume Sampler
Methane Analyzer (Xmethane)
Sample (Air + Methane)
Flow Measurement Vsample
Variable Speed Blower
Mixing Orifice
Methane Calculation
  Vmethane = Xmethane * Vsample – Vmethane_bkgd
  Flow measurement accuracy
  Analyzer accuracy
  Vmethane_bkgd typically 1.5-3 CF per 1,000 MCF
  Methane concentration of 13,700 ppm given
    0.137 CFM methane leak (0.4% or 198 CF)
    10 CFM sample flow

## Slide 9: Methane Quantification: Enclosure Methods
Enclosure placed around component (tank, valve, vehicle, pump, station)
Ambient background air drawn through enclosure at controlled/measured rate
Methane concentration of sample measured

## Slide 10: Methane Quantification: Enclosure Methods
Enclosure (bag) around potential leak site
Sample mass flow measured
Methane analyzer used to measure sample concentration
Methane leak example:
  Sample flow = 0.28 l/min
  Sample methane concentration = 10.32 ppm
  Background methane concentration = 2.93 ppm
  Leak Rate = 1.47 grams per minute
Sample Methane Concentration and Flow

## Slide 11: Basic Atmospheric Sampling Analysis
Assumptions
  30 foot high by 300 foot wide sample planes (9,000 square feet)
  Sample planes located 300 feet upstream and 300 feet downstream from leak site
  Methane leak rate of 0.137 CFM
  Wind speed of 5 mph (440 feet per minute) perpendicular to sample planes
Volume flow through samples planes is 3,960 MCF per minute (9,000 ft2 x 440 ft per minute)
Upstream plane is at background concentration (1.5-3 ppm)
Average methane concentration in downstream plane is increased 0.034 ppm (2.3% to 1.1%)

## Slide 12: Atmospheric Methods
Measure upwind and downwind methane concentrations
Mass fluxes quantification
  Volume flux
    Micrometeorological models
    Tracer gas
  Methane Concentrations
    Point source(s) sampling
    Line (plane) detection
Sniffer or high-volume sampling required for identification/quantification of individual sources
Wind speed/direction requirements
Loss levels of interest may still yield low concentrations
12

## Slide 13: Quantification by Mass/Volume Metering
Masses or volumes of fuel supplied to and delivered by facility compared
Measurement accuracy:
  Mico-motion metering accuracy: +/- 0.5%
  Utility meter accuracy: -2%-+1%
  Accuracies are at or above the loss of interest (0.4%)
Methane content of fuel is not known
  Peak shaving gases in some regions may be very low in methane
13

## Slide 14: Fueling and Maintenance Surveys
Responses to verbal interviews, questionnaires and inventories with respect to fueling and maintenance procedures
  Fueling facility practices
    Vehicles fueled
    Fuel quantities delivered
    Fueling frequencies
  Fueling equipment, procedures and storage
  Fleet inventory with engine/fuel system information
  Natural gas released during vehicle maintenance
  Vehicle storage practices
  Use of recovery equipment

## Slide 15: Methane Inventory Model
Predictive spreadsheet model
  Estimates of nationwide contribution from heavy-duty transportation sector
  Default values included
    Fleet population
    Fueling station population
    Activity and event frequencies
    Emissions data
  User values for improved estimates
  Outputs
    Mass per year
    Nationwide mass per year
    Mass per vehicle per year
    Mass per vehicle mile travelled

## Slide 16: Facility Measurements
Preliminary evaluations
  Two fueling stations, one CNG and one LNG
  “Bottom up” approach (high-volume sampling) and upwind/downwind
  Results presented to TAP before proceeding
Detailed evaluations
  Four refueling stations and two maintenance facilities
  Leak detection and quantification
  High-volume/enclosure measurements of each leak
  Quantification of intermittent leaks (eg. refueling)
  Vehicle tailpipe methane emissions screening
Standard evaluations
  Four refueling stations and two maintenance facilities
  Leak detection and quantification with high-volume sampling
16

## Slide 17: Procedures for Facility Emissions
Initial Site Visit
  Survey and document/inventory site
  Develop test plan
  Confirm test plan with technical advisory panel and steering committee
Site Evaluation
  Transport personnel and equipment to site
  Calibrate/verify test equipment
  Interview operational personnel
  Perform facility methane emission detection
  Perform facility methane emission quantification
  Refueling/Maintenance methane emissions quantification
Review and archive data
17